## Slide 1
Redis
Detection Algo Module
MQTT Module
GPIO Module
MQTT Server
RPi 1
RPi 2

## Slide 2
Algo
Redis
MQTT
GPIO
Redis Publish: tester.vid<ID>.result
tester.vid<ID>.result: {‘cat’: <str>, ‘val’: <str/int>
GPIO output such as LED, Servo or bipper
tester.vid<ID>.response: {‘status’: success/failed, ‘cat’: <str>, ‘val’: <str/int>}
tester.vid<ID>.response: {‘status’: success/failed, ‘cat’: <str>, ‘val’: <str/int>}
Deliver to MQTT server
Message flow:
  Algo send detection result with category and value
  Redis received message and capture by GPIO adaptor
  GPIO plugin module extract info and output to LED, Servo or bipper depending on message content
  GPIO send response message to Redis contain hardware update status, category and value
  Message capture by MQTT module and deliver to MQTT server
Every minutes, Algo need to deliver tester.vid<ID>.status message indicate usage condition and utilization rate